T.Moore
2.6.19
Notes taken from webpage: http://wiki.seeedstudio.com/Grove_Base_Hat_for_Raspberry_Pi/
GIT Project Directory: https://github.com/Seeed-Studio/grove.py

Grove Base Hat For RPI Library Setup
Step1:

$$ curl -sL https://github.com/Seeed-Studio/grove.py/raw/master/install.sh | sudo bash -s -

Step2:
If everything goes well you should get:
Successfully installed grove.py-0.5
#######################################################
Lastest Grove.py from github install complete !!!!!
#######################################################

Step3:
You can check the source file by cloning the grove.py library.
$$ git clone https://github.com/Seeed-Studio/grove.py

Usage
To use the grove modules, type..
$$ grove <TAB> to see the supported grove list of modules. For example:
pi@raspberrypi:~$ grove_
grove_3_axis_compass_bmm150 grove_i2c_color_sensor_v2 grove_mini_pir_motion_sensor grove_rotary_angle_sensor grove_temperature_sensor
grove_4_digit_display grove_i2c_motor_driver grove_moisture_sensor grove_ryb_led_button grove_thumb_joystick
grove_air_quality_sensor_v1_3 grove_lcd_1.2inches grove_oled_display_128x64 grove_servo grove_tilt_switch
grove_button grove_led grove_piezo_vibration_sensor grove_slide_potentiometer grove_touch_sensor
grove_collision_sensor grove_light_sensor_v1_2 grove_pwm_buzzer grove_sound_sensor grove_ultrasonic_ranger
grove_gesture_sensor grove_loudness_sensor grove_recorder_v3_0 grove_switch grove_water_sensor
grove_high_accuracy_temperature grove_mech_keycap grove_relay grove_temperature_humidity_sensor
pi@raspberrypi:~$ grove_

DIGITAL PORT Usage (Ultrasonic ranger):
$$ grove_ultrosonic_ranger 5 6
For most grove module, you need to add the pin number parameter, like:

$$ grove_ultrasonic_ranger 5 6

5 and 6 are the GPIO/BCM pin. However, you may have noticed that in the first example:

grove_pwm_buzzer
we didn't add a parameter after the command. This is because the PWM port and I2C port do not require pin number parameters. You can find the pin number silkscreen just besides the Grove sokect.

ANALOG PORT USAGE (air quality sensor):
$$ grove_air_quality_sensor_v1_3 0 1

Make sure to use the pin # designations (0, 1) not the port # (A0, A1)

I2C PORT USAGE (OLED Display 128x64):
pi@raspberrypi:~$ grove_oled_display_128x64
pi@raspberrypi:~$

This will display the ‘hello world’ on the OLED.